## Slide 1: 生醫量測系統設計 Design of Biomedical Measurement Systems
LAB 1
ECG&PPG signal extract

## Slide 2: Hardware
The hardware used in this project is as below.
1. ECG 6 click 2. NUCLEO-F401RE
Notes: 這堂課第一個assignment我們會用到xxx和xxx板子，左邊這塊可以讀取ECG訊號也可以讀取到PPG訊號，稍後會在介紹什麼是ECG和PPG

## Slide 3: System Architecture

## Slide 4: Development Environment
STM32CubeIDE
ANACONDA
VsCode
Notes: 會使用到的工具

## Slide 5: Development Environment
Code Generation and Compile and Burn
Build Virtual Environment
Code Editor
Notes: 虛擬環境為什麼需要

## Slide 6: ANACONDA
Build Environment
  conda create --name python38 python=3.8
  Enter y to proceed

## Slide 7: ANACONDA
Build Environment
  conda info --env (you will see the python38)
  conda activate python38 (base will change to python38)

## Slide 8: ANACONDA
After entering the virtual environment, enter the following command to complete the module installation.
  pip install scikit-learn
  pip install pyserial
  pip install numpy
  pip install PyQt5
  pip install matpltlib
After entering the command, you will receive a message as below.

## Slide 9: ANACONDA
Use “cd” command to enter the directory.
Use “python” command to execute the python code.

## Slide 10: Electrocardiography
Electrocardiography(ECG) is a graph of heart electrical signals. In this project, we will use lead 1.
You can get lead 1 ECG by placing electrodes on the left arm, right arm, and left foot.
Notes: 根據Lead 1規則後面會再做詳細介紹

## Slide 11: Photoplethysmography
Photoplethysmography(PPG) is a method to measure the blood volume in blood vessels. We can use LED and photodiode to obtain the signal.
Notes: 光積體變化描技法（Photoplethysmography，簡稱PPG）是一種非侵入性的方法，用於檢測組織微血管中的血容量變化。通常用於監測心率和其他生命體徵。基本的設置包括將光線照射到皮膚中，並測量經過或反射的光的量來得到生理訊號
非接觸式RPPG實驗室得東西有興趣可以稍後來問

## Slide 12: Data Preprocessing
After receiving the data from MAX86150, the data needs to be processed first. This step calls “preprocessing”.

## Slide 13: COM port
Directly connect using USB
  From 'Control Panel' to 'Device Manager'
  Locate 'Ports (COM & LPT)' and check

## Slide 14: ECG electrode position
R L
RA
LA
LL (Can also be placed on the left abdomen or left foot)

## Slide 15: 生醫量測系統設計 Design of Biomedical Measurement Systems
LAB 2
Model Training And Validation

## Slide 20: Heart Disease Recognition
Cut Data
Train Model
Visualization
Prepare Data
ECG 1
ECG 2
ECG 43
ECG 1
250
250
250
MIT-BIH Dataset
ECG 1~43 use for training ECG 44 use for inference

## Slide 21: Heart Disease Recognition
Cut Data
Train Model
Visualization
Prepare Data
ECG 1
ECG 2
ECG 43
ECG 1
250
250
250
MIT-BIH Dataset
ECG 1~43 use for training ECG 44 use for inference

## Slide 22: MIT-BIH Arrhythmia Database
The MIT-BIH Arrhythmia Database contains 48 half-hour excerpts of two-channel ambulatory ECG recordings, obtained from 47 subjects studied by the BIH Arrhythmia Laboratory between 1975 and 1979.
The recordings were digitized at 360 samples per second per channel with 11-bit resolution over a 10 mV range. Two or more cardiologists independently annotated each record; disagreements were resolved to obtain the computer-readable reference annotations for each beat (approximately 110,000 annotations in all) included with the database.

## Slide 23: Label & Description

## Slide 24: Heart Disease Recognition
Cut Data
Train Model
Visualization
Prepare Data
ECG 1
ECG 2
ECG 43
ECG 1
250
250
250
MIT-BIH Dataset
ECG 1~43 use for training ECG 44 use for inference

## Slide 25: ECG Signal Cutting

## Slide 26: Model Training
Cut Data
Train Model
Visualization
Prepare Data
ECG 1
ECG 2
ECG 43
ECG 1
250
250
250
MIT-BIH Dataset
ECG 1~43 use for training ECG 44 use for inference

## Slide 27: CNN
Convolution: Extracting features from an image by sliding a kernel, with the control of image dimensions through strides and padding.
https://cinnamonaitaiwan.medium.com/%E6%B7%B1%E5%BA%A6%E5%AD%B8%E7%BF%92-cnn%E5%8E%9F%E7%90%86-keras%E5%AF%A6%E7%8F%BE-432fd9ea4935

## Slide 28: CNN
Different strides result in variations in the output feature map sizes.

## Slide 29: CNN
Padding (Same Padding or Valid Padding):
  1. Same Padding will keep the output Feature map and the input image the same size.
  2. Valid Padding will not pad the edges, so the Feature map size will decrease.

## Slide 30: Model Training
Accuracy 95% or more Output Model Size is less than 2MB, otherwise the board will not fit.

## Slide 31: Model Parameters
(3*3*3+1)*16 = 448
(3*3*16+1)*32 = 4640
(3*3*32+1)*64 = 18496
(78400+1)*512 = 40141312
(512+1)*1 = 513

## Slide 32: Model Parameters
https://blog.csdn.net/qq_41573860/article/details/116767639
https://blog.csdn.net/w_x_yhao/article/details/123050474
(3*3*3+1)*16 = 448
(3*3*16+1)*32 = 4640
(3*3*32+1)*64 = 18496
(78400+1)*512 = 40141312
(512+1)*1 = 513
40,165,409

## Slide 33: Visualization
Cut Data
Train Model
Visualization
Prepare Data
ECG 1
ECG 2
ECG 43
ECG 1
250
250
250
MIT-BIH Dataset
ECG 1~43 use for training ECG 44 use for inference

## Slide 34: Visualization

## Slide 35: Visualization

## Slide 36: Confusion Matrix
How to identify the quality of a model?
https://www.maxlist.xyz/2022/09/12/confusion-matrix/

## Slide 37: Overfitting
https://ithelp.ithome.com.tw/m/articles/10203371

## Slide 38: Overfitting
https://ithelp.ithome.com.tw/m/articles/10203371

## Slide 39: Overfitting
https://wenkangwei.github.io/2020/11/13/DL-DropOut/

## Slide 40: Visualization

## Slide 41: 生醫量測系統設計 Design of Biomedical Measurement Systems
LAB 3
Convert Model To .tflite

## Slide 42
Why TFLite ?
https://ithelp.ithome.com.tw/m/articles/10272501

## Slide 43
The library generated through TFLite has a small footprint, which is crucial for smartphones or MCU with limited storage space.
Notes: 通過 TFLite 生成的依賴庫體積很小 (在寸土寸金的手機儲存空間這很重要)

## Slide 44
It supports hardware acceleration on mobile devices and can run on both Android and iOS platforms.
Notes: 支援手機端硬體加速

## Slide 45
Model is smaller we will show you later.
Notes: 支援手機端硬體加速

## Slide 46: Change Model Type
.tflite model is smaller than .h5 model

## Slide 47: 生醫量測系統設計 Design of Biomedical Measurement Systems
LAB 4
Quantize Model To Smaller Size

## Slide 48: STM32cubeIDE
STM32CubeIDE is the official IDE released by STMicroelectronics for STM32 development. It combines features such as development board selection, program coding, compilation, and flashing, eliminating the need for switching between software and configuring environments.

## Slide 49: Create STM32 Project

## Slide 50
Create STM32 Project

## Slide 51
Create STM32 Project
Notes: 左邊是IDE編譯器，自動產生的底板程式碼，
右邊是CUBEMX軟體介面，可對開發板硬體資源進行設定。

## Slide 52
Install X-CUBE-AI
Notes: 下載AI開發所需的software packs

## Slide 53
Install X-CUBE-AI

## Slide 54
Select X-CUBE-AI

## Slide 55
Select X-CUBE-AI

## Slide 56: Reset and clock control (RCC)
Notes: RCC 的完整英文描述是 ，Reset and clock control，重置(system, power, and backup reset)與時脈控制。
高速外部時脈訊號 (HSE)
低速外部時脈訊號 (LSE)
Crystal/Ceramic Resonator（石英/陶瓷 晶振）

## Slide 57: UART

## Slide 58: UART

## Slide 59: Add Network and Analyze

## Slide 60: Add Network and Analyze

## Slide 61: Model Quantization
Model quantization is an optimization technique for deep learning models aimed at reducing storage space and computational resources while preserving predictive performance.
Notes: 模型量化（Model Quantization）是一種深度學習模型優化技術，旨在減少模型佔用的存儲空間和計算資源，同時保持模型的預測性能。

## Slide 62: Model Quantization
The primary principle of this technique involves reducing the precision of weights and activation values in the model, typically converting them from floating-point numbers to lower-bit integer representations.
Notes: 這種技術的主要原理是減少模型中權重和激活值的位數，通常是由浮點數轉換為更低位數的整數表示。

## Slide 63: Model Quantization
Weight Quantization: Transformed from floating-point numbers to integer representations. This transformation often uses lower-bit integers, such as 8-bit or 16-bit integers.
Notes: 在模型量化中，通常將原始模型中的浮點數權重轉換為整數表示。這種轉換通常使用較低位數的整數，例如8位或16位整數。這樣的轉換減少了權重的存儲需求，同時仍然可以保持模型的相對性能。

## Slide 64: Model Quantization
Quantization during Training and Dequantization during Inference: This is done to realize the benefits of quantization during training while not compromising the predictive performance of the model during inference.
Notes: 在訓練過程中，模型權重和激活值被量化為較低位數的整數。但在實際推理（預測）過程中，通常仍然使用浮點數進行計算。這樣做是為了在訓練時實現量化的好處，同時在推理時不損失模型的預測性能。

## Slide 65: Model Quantization
Hardware Support: Some hardware, such as specific GPUs, TPUs, or DSPs, can efficiently handle integer operations. This further enhances the benefits of model quantization, leading to faster inference speeds on hardware.
Notes: 硬體支援： 一些硬體（如特定的GPU、TPU或DSP）能夠更有效地處理整數運算，這進一步提高了模型量化的效益，使得在硬體上的推理速度更快。

## Slide 66: Representative Data
A subset of data that accurately reflects the characteristics and distribution of the overall dataset.
Notes: 是指一個數據集的子集，能夠準確反映整體數據集的特徵和分佈

## Slide 67: Representative Data
When working with large datasets, it may be computationally expensive. In such cases, a representative sample or subset of the data is selected to stand in for the entire dataset.
Notes: 在處理大型數據集時，使用整個數據集進行各種任務，如模型訓練、驗證或測試，可能會計算上昂貴或不切實際。在這種情況下，選擇一個代表性的樣本或子集來代表整個數據集。

## Slide 68: Representative Data
In tools like TensorFlow Lite, it is common practice to use a representative dataset for model quantization. By using such a representative dataset, it can be ensured that the quantized model better retains its predictive capabilities during the conversion process.
Notes: 在 TensorFlow Lite 等工具中，常見的做法是使用代表性數據集合（representative dataset）來量化模型。這個數據集合包含了一些特定於應用的樣本，這些樣本可以代表模型在部署時將要處理的數據。透過這樣的代表性數據集合，可以確保量化模型在轉換過程中更好地保留其預測能力。

## Slide 69: Representative Data

## Slide 70: Shrink Model
Use quantized method can shrink .tflite model

## Slide 71: Change Model and Analyze

## Slide 72: Analyze Output
The tool will infer the model's resource occupancy (ROM, RAM) based on the model and model parameters, allowing an assessment of whether the model can be deployed to a development board.

## Slide 73: Validation on desktop
The verification data is the testx.npy and testy.npy files we just specified.

## Slide 74: Validation on desktop
To verify the training model, we mainly verify the differences in computing resources, model accuracy, etc. before and after the verification between the original model and the model converted to C language support.
Notes: 沒有Accuracy 是因為我們範例使用的模型不是分類模型是回歸模型

## Slide 75: Generate Code

## Slide 76: Build Project

## Slide 77: Build Project

## Slide 78: Build Project

## Slide 79: Validation on target
The verification data is the testx.npy and testy.npy files we just specified.

## Slide 80: Validation on target
The model is successfully verified on the target board.